## Slide 1
How we measure
1
Capture
4 faces
2
Face and edge
mask, corners
3
Scale
ArUco marker
4
Flatten
homography
5
Measure
10 lines
1 Capture and scale
Photos of front, back, left and right (top optional), each square-on to the face
A printed ArUco marker of known size sits flat on the face
OpenCV finds the marker's four corners
cm per pixel = real marker size ÷ marker side in pixels (about ±2–5%)
2 Face and edge
MobileSAM (or a small YOLO-seg model) on ONNX Runtime cuts the block face out of the photo as a mask
OpenCV findContours traces the edge with 12–24 points, following chips
approxPolyDP gives the four corners of the face
3 Flatten and measure
getPerspectiveTransform maps the four corners to a true rectangle in cm, so the photo angle no longer matters
Ten lines are laid across the flat face and measured edge to edge (slide 3)
Lengths are averaged per face, then across faces
Length × width × height = volume · volume × 2.7 t/m³ = weight
Notes: Five steps left to right. Scale comes from a printed ArUco marker of known size: cm per pixel is the marker's real size divided by its side in pixels. The face is cut out with a segmentation model run through ONNX Runtime on the CPU, and OpenCV turns the mask into an edge and four corners. A perspective transform flattens the face into a true rectangle, then ten lines are measured across it. Length comes from front and back, width from left and right, height from all four. Volume is length times width times height and weight is volume times density, 2.7 tonnes per cubic metre by default.

## Slide 2
How we check holes and cracks
What is flagged on each photo
MINOR
Cosmetic marks, soil and dust that washes off. Shown and listed in the report.
MAJOR
Local damage near the surface. A box with a safety margin is drawn, and that part is left out of the usable stone.
REJECT
A crack, void or hole that splits or hollows the block. The whole region is excluded and the block is flagged for review.
Open-source detection (CPU)
1
Trained detector
YOLOX or YOLO-nano, exported to ONNX and run with ONNX Runtime. Classes: crack, hole, void, chip, vein, soil. Trained on 300–500 labelled quarry photos per class, with a separate test set.
2
OpenCV filter
Grey, even out the light (CLAHE), highlight thin dark lines (black-hat), Canny edges, keep long thin connected shapes as cracks and dark round blobs as holes.
3
Severity rules
Size and position decide MINOR, MAJOR or REJECT: a crack that crosses the face or a large hole is REJECT.
4
Used in the result
Boxes are drawn on the photo and listed. MAJOR and REJECT regions are removed before the 10 lines are laid, so lines only measure sound stone.
Only visible surface defects can be found. The bottom face and the inside of a block cannot be judged from photographs, so the report says so.
Notes: Three severities. MINOR is listed only. MAJOR and REJECT are boxed and taken out of the usable stone. The detector is a small YOLO-family model exported to ONNX so it runs on a normal CPU. It is only as good as its training photos, so collect and label real quarry photos and keep a separate test set. The OpenCV filter is a fallback that needs no training: black-hat finds thin dark lines, Canny finds edges, and a length-to-width test keeps cracks. It can also pick up veins and saw marks, so a person should confirm.

## Slide 3
How the 10 lines are made
1
2
3
4
5
6
7
8
9
10
A face with a chipped corner: lines 6 to 10 come out shorter. The arrow is the face height, split into 10 equal gaps.
1
Flatten the face
The four corners map to a true rectangle in cm, so the angle of the photo does not stretch the lines.
2
Find the height
Top of the traced edge to its bottom, on the flat face.
3
Split into 10 gaps
gap = height ÷ 10
4
Place the lines
line i is at top + (i + 0.5) × gap. Its length is where it meets the left and right edge.
5
Average
The 10 lengths give the face length. Faces are averaged for the block: length from front and back, width from left and right.
Example: height 100 cm, gap 10 cm. Lengths 240, 240, 240, 240, 240, 230, 209, 200, 200, 200 cm, average 223.9 cm
Notes: Why ten lines: a rough face is not a perfect rectangle, so two edges can hide a chip. Ten lines follow the real edge and their average is more representative. Lines 1 to 5 here run the full width and lines 6 to 10 are shorter because of the chip. The lines are placed on the flattened face, so a photo taken a little off-centre does not make the far end look shorter. Height is simply ten gaps added up, so no separate height lines are needed. Pure geometry with NumPy and OpenCV, no model involved.

## Slide 4
Conclusion
OpenCV
Apache-2.0
Corners, contours, flattening, ArUco
ArUco marker
in OpenCV
Known-size scale, about ±2–5%
MobileSAM
Apache-2.0
Cuts the block face out of the photo
YOLOX / YOLO-nano
Apache-2.0 / small
Cracks, holes and chips
ONNX Runtime
MIT
Runs the models on a plain CPU
NumPy + FastAPI
BSD / MIT
The 10-line maths and the service
CPU only
no GPU, works offline
±2–5%
scale from a printed marker
No per-call cost
once the models are in place
Next steps
Make the marker mandatory in every photo
Label 300–500 face and defect photos per class
Train and export the two small models to ONNX
Compare with tape on 30–50 blocks to report the real error
Notes: The whole pipeline uses open-source software that runs on a CPU: OpenCV for corners, flattening and the marker, MobileSAM for the face mask, YOLOX or YOLO-nano for cracks and holes, ONNX Runtime to run the models, and NumPy with FastAPI for the maths and the service. Confirm each licence against the exact version used before deployment. Accuracy depends mainly on scale, which is why the marker is mandatory. The tape comparison on 30 to 50 blocks gives the real error to report.